APPENDIX I

Feasibility Evaluation by Element

This section contains essentially the same information as Appendix J but is organized in terms of element rather than by measurement technique.  The measurability of a specific element is listed as well as the possible techniques.  Specific mention is made of key isotopic abundance measurements. Required precision is 10% for elemental abundances and 1% for isotopic abundances except for CNO where 0.1% is the target goal.  Further study of RIMS background is required, but it is conceivable that all elements except F and the noble gases can eventually be analyzed with RIMS.

H	Data from solar wind regime monitor and from nuclear reaction depth profiling; diffusion losses from collectors may be important but overall would be an advantage in minimizing H interferences with analysis of other elements.

He	Noble gas mass spectrometry gives both abundance and isotopic composition; comment on H diffusion loss applies to He also

Li 	The abundance and important constraints on the isotopic composition can be obtained by SIMS and possibly RIMS

Be 	possibly RIMS

B 	Sufficient sensitivity with SIMS or RIMS, but surface contaminations very severe; can possibly be overcome by using concentrator target material

C 	Abundance by SIMS; isotopic composition by SIMS and/or static gas mass spectrometry; sensitivity exists for collector foils, but because of serious contamination problems, concentrator target material may be required

N	Abundance and isotopic abundance measurement by gas mass spectrometry, sensitivity exists for analysis of collector foils, but because of surface contamination problems, concentrator target material may be required

O 	Possibly abundance and 18O/16O by SIMS and static gas mass spectrometry; surface contamination problems require measurement on concentrator target material; this is highest priority in concentrator design

F 	Abundance with SIMS

Ne	Abundance and isotopic composition by noble gas mass spectrometry

Na	Abundance by SIMS, RIMS, or neutron activation; serious surface contamination problems

Mg 	Abundance and isotopic composition by SIMS or RIMS

Al 	Abundance by SIMS or RIMS

Si	Abundance and isotopic composition by SIMS; abundance by RIMS

P	Same as Al

S 	Abundance and isotopic composition by SIMS, except that 36S/32S precision will be about 3%

Cl 	Abundance by SIMS

Ar	Abundance and isotopic composition by noble gas mass spectrometry

K	Abundance by SIMS and RIMS; serious surface contamination problems

Ca 	Abundance and isotopic composition by SIMS, but precision of 43Ca and 46Ca worse than 1%; abundance by RIMS

Sc 	Abundance by neutron activation, SIMS, and RIMS.

Ti 	Abundance and isotopic composition by SIMS and RIMS

V 	Abundance by SIMS and RIMS

Cr	Abundance by SIMS or RIMS

Mn	Same as Cr

Fe	Same as Cr

Co	Same as Cr

Ni	Same as Cr

Cu	Abundance by SIMS, neutron activation, possibly RIMS

Zn	Same as Cu

Ga	Same as Cu

Ge	Same as Cu

As	Abundance by neutron activation, possibly RIMS

Se	Abundance by SIMS

Br	Abundance by SIMS and by neutron activation

Kr	Abundance and isotopic composition by noble gas mass spectrometry

Rb	Abundance by neutron activation and by SIMS; possibly isotopic abundance by SIMS; abundance and isotopic composition by RIMS

Sr	Abundance by SIMS and RIMS

Y	Abundance by SIMS and RIMS

Zr	Abundance by SIMS and  RIMS

Nb	RIMS

Mo	Abundance by neutron activation, RIMS, and possibly by SIMS

Ru	Abundance by neutron activation and RIMS

Rh	RIMS

Pd	neutron activation and RIMS

Ag	neutron activation and RIMS; serious contamination problems

Cd	neutron activation and RIMS

In	RIMS, serious contamination problem

Sn	RIMS

Sb	neutron activation and RIMS

Te	Abundance by neutron activation

I	Abundance by SIMS

Xe	Abundance and isotopic composition by noble gas mass spectrometry

Cs 	Abundance by neutron activation, RIMS, possibly SIMS.

Ba 	Abundance by SIMS, RIMS, and neutron activation

Rare earth elements:

Neutron activation for La, Ce, Nd, Sm, Eu, Tb, Ho, Yb, Lu; all possibly with RIMS

Hf	Abundance by neutron activation, RIMS

Ta	Abundance by neutron activation, RIMS

W	RIMS, possibly by neutron activation

Re	RIMS, possibly neutron activation

Os 	Abundance by neutron activation and RIMS

Ir	Abundance by neutron activation and RIMS

Pt	RIMS

Au	Probably not possible as large quantities of Au used in canister design; deliberately sacrificed element

Hg 	Abundance by neutron activation; Severe contamination problems.

Tl 	Possibly by neutron activation

Pb 	Probably not analyzable; severe contamination

Bi	Probably not analyzable

Th	Abundance by neutron activation and RIMS

U	Very rare, possible if truly zero-background RIMS can be designed